Open Geospatial Consortium	OGC Doc 08-121

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | OWS Common | CR | 08-121 | ( rev | - | ( Current version: | 1.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | OWS Common 1.1 Change Request – Add Temporal Conventions to address TimeZone Offset Request and Service handling. |
| Source: ( | James Ressler, Northrop Grumman; Dave Wesloh, NGA |
| Work item code: ( |  |  | Date: ( | 2008-08-15 |
| Category: ( | B |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | The Time Zone for temporal data is not standard in data sources but knowledge of the time zone is necessary for consistent queries and unambiguous results, especially queries that encompass data from multiple time zones or filter by the hour, minute or second. |
| Summary of change: ( | Implement a default time zone of UTC as defined by ISO 8601:2004 and ISO 8601:2000 (or Greenwich Mean Time, also referred to as “Z” for Zulu Time) for all temporal data passed or returned to/from OGC Web Services. ISO 8601 accounts for local time by specifying an offset to UTC. Default conventions for specifying time zone by client and services are specified. Web services should allow the client to request a time zone offset to be applied to all temporal data through a parameter passed on operations. For example, if the client requested all data referenced in U.S. eastern time zone, a time zone offset of -0500 (five hours) from UTC would be applied to all temporal fields. The web service must able to convert and return temporal data values from the time zone of the data to the specified time offset given in the request. |
| Consequences if ( not approved: | Inconsistent temporal queries and ambiguous results, especially temporal queries that encompass data from multiple time zones. |
| Clauses affected: ( | Section 10, Other operation parameters |
| Other specs ( | x | Other core specifications ( | Any dependant upon OWS Common 1.2 |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( | Change pages to OWS Common specification included. |
| Other comments: ( | The WMS profile of ISO 8601 in WMS Annex D is specific to WMS. The WMS profile examples should be embellished to conform to this change request. |

Open Geospatial Consortium Inc.

Date: 2008-08-15

Reference number of this OGC™ document: OGC 08-121

Version: 1.2

Category: OGC™ Implementation Specification

Editor: Arliss Whiteside

OGC Web Services Common Specification

Change request document 08-121 Temporal Conventions

Copyright © Open Geospatial Consortium (2008)

## Temporal Conventions

Client requests with temporal parameters (such as WMS Time or WFS filter constraints) shall be expressed in valid ISO 8601:2004 and ISO 8601:2000 temporal expressions.

OGC Web Service responses with temporal data shall be expressed in valid ISO 8601:2004 and ISO 8601:2000 temporal expressions.

### Time Zone Offset

The following conventions apply to the processing of temporal information with respect to time zones.

When time zone offsets are used in a temporal element of a client request, the server processing the request shall interpret temporal information with respect to the client’s requested time zone.

When there is no time zone offset expressed in a temporal element, an OGC web service shall assume a UTC zone (also referred to as “Z” or Zulu time).

The local time zone of client or server shall not be assumed; it shall either be explicitly stated as an offset or assumed to be UTC.

All service responses with temporal information shall include the “Z” designation for UTC time zone or a time zone offset, according to ISO 8601.

Data from multiple time zones in the same service request or response shall be represented with time zone offset.

An optional request parameter TIMEZOFFSET and schema element timeZOffset shall be included in client requests for temporally referenced information to specify the time zone of the results.

A web service shall convert and return data in the same time zone as the requested temporal parameters or the TIMEZOFFSET/timeZOffset value in the request, where TIMEZOFFSET/timeZOffset has precedence. If multiple time zones exist in the requested temporal parameters, the zone returned shall be UTC.

An example implementation of the time zone convention is depicted in figure 10.8.1-1. The results provided to the client are in Geneva’s time zone offset. Because the client requested a time zone offset of “+01”, the results are not returned in UTC, or the web service’s local time zone, or database server’s local time zone. In this example, because the database implementation uses a local time, conversion from local time to UTC is required by the database and to client’s time zone by the service.

Figure 10.8.1-1: Time Zone Offset Inter-Zone Web Service Request