Open Geospatial Consortium	Document OGC 08-089r3

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | AS Topic 2 | CR | ? | ( rev | - | ( Current version: | OGC 08-015 |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS | X | Imp Spec |  | Best Practices Paper |  | Other |  |
| Title: ( | Topic 2 change request - Correct inconsistencies |
| Source: ( | Arliss Whiteside |
| Work item code: ( |  |  | Date: ( | 2008-09-12 |
| Category: ( | C |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | Table 4 of OGC Abstract Specification Topic 2 (OGC 08-015, which copies ISO 19111:2007) does not list two important association roles, and is thus inconsistent with Figure 6 which shows those roles. Similarly, Table 42 does not list two association roles, and is thus inconsistent with Figure 11. Table 49 lists the stereotype as CodeList instead of Union, and is thus inconsistent with Figure 12. Also, Figures 5 through 12 do not show some classes as being abstract, and are thus inconsistent with the tables for these classes. |
| Summary of change: ( | List two more association roles in Tables 4 and 42 to agree with Figures 6 and 11. Correct the stereotype listed in Table 49 to agree with Figure 12. Identify some classes as abstract in Figures 5 through 12 to agree with corresponding tables. |
| Consequences if ( not approved: | Continued inconsistencies in OGC Abstract Specification Topic 2, leading to mistakes and wasted time |
| Clauses affected: ( | Tables 4, 42, and 49, Figures 5 through 12 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Papers |  |
| Supporting Doc. ( |  |
| Other comments: ( | In the absence of editable figure graphics, this change request proposes table notes that state the figure errors using text. |
| Status ( |  |
| Disposition ( |  |

Edit Tables 4, 42, and 49 in OGC 08-015 as follows:

Table 4 — Defining elements of SC_CRS class

| Description: Coordinate reference system which is usually single but may be compound. |
| --- |
| Stereotype: Type Class attribute: Abstract Inheritance from: RS_ReferenceSystem IO_IdentifiedObjectBase Association roles: sourceCRS from CC_CoordinateOperation [0..1], association named Source targetCRS from CC_CoordinateOperation [0..1], association named Target coordinateOperationFrom to CC_CoordinateOperation [0..*], association named Source coordinateOperationTo to CC_CoordinateOperation [0..*], association named Target CRS from GM_Object [0..1], association named Coordinate Reference System (reverse: object to GM_Object [0..*] navigable only from GM_Object – see ISO 19107) CRS from DirectPosition [0..1], association named Coordinate Reference System (reverse: directPosition to DirectPosition [0..*] navigable only from DirectPosition – see ISO 19107) Public attributes: |
| Attribute name | UML identifier | Data type | Obligation | Maxi-mum Occur-rence | Attribute description |
| CRS scope | scope | CharacterString | M | N | Description of usage, or limitations of usage, for which this CRS is valid. If unknown, enter “not known”. |
| The following 5 attributes are inherited from IO_IdentifiedObjectBase and from RS_ReferenceSystem – see Tables 1 and 3. NOTE As an exception to elsewhere in this Abstract Specification, inherited attributes are included in this class table to allow the CRS name, CRS alias and CRS identifier attributes to be shown together. |
| Attribute name | UML identifier | Data type | Obligation | Maxi-mum Occur-rence | Attribute description |
| CRS name | name | RS_Identifier | M | 1 | This is the primary name for the CRS. Aliases and other identifiers may be given through the attributes alias and identifier. |
| CRS alias | alias | GenericName | O | N | An alias by which this CRS is known. |
| CRS identifier | identifier | RS_Identifier | O | N | An identifier which references elsewhere the CRS's defining information; alternatively an identifier by which this CRS can be referenced. |
| CRS validity | domainOfValidity | EX_Extent | O | N | Area or region or time frame in which this CRS is valid. |
| CRS remarks | remarks | CharacterString | O | 1 | Comments on or information about this CRS, including data source information. |

Table 42 — Defining elements of CC_CoordinateOperation class

| Description: A mathematical operation on coordinates that transforms or converts coordinates to another coordinate reference system. Many but not all coordinate operations (from CRS A to CRS B) also uniquely define the inverse coordinate operation (from CRS B to CRS A). In some cases, the coordinate operation method algorithm for the inverse coordinate operation is the same as for the forward algorithm, but the signs of some coordinate operation parameter values have to be reversed. In other cases, different algorithms are required for the forward and inverse coordinate operations, but the same coordinate operation parameter values are used. If (some) entirely different parameter values are needed, a different coordinate operation shall be defined. |
| --- |
| Stereotype: Type Class attribute: Abstract Inheritance from: IO_IdentifiedObject Association roles: sourceCRS to SC_CRS [0..1], association named Source targetCRS to SC_CRS [0..1], association named Target coordinateOperationFrom from CC_CoordinateOperation [0..*], association named Source coordinateOperationTo from CC_CoordinateOperation [0..*], association named Target (aggregation) coordOperation from CC_ConcatenatedOperation [2..*] {ordered} (reverse: concatOperation to CC_ConcatenatedOperation [0..*] navigable only from CC_ConcatenatedOperation – see Table 46) coordOperation from CC_PassThroughOperation [1] (reverse: passThruOperation to CC_PassThroughOperation [0..*] navigable only from CC_PassThroughOperation – see Table 47) (associations inherited from IO_IdentifiedObject) Note attached to associations Source and Target: The “sourceCRS” and “targetCRS” associations are mandatory for coordinate transformations only. Coordinate conversions have a source CRS and a target CRS that are NOT specified through these associations, but through associations from GeneralDerivedCRS to SingleCRS. For a concatenated coordinate operation sequence of n coordinate operations: source CRS (concatenated coordinate operation) = source CRS (coordinate operation step 1) target CRS (coordinate operation step i) = source CRS (coordinate operation step i + 1); i = 1 ...(n ( 1) target CRS (concatenated coordinate operation) = target CRS (coordinate operation step n) Instead of a forward coordinate operation, an inverse coordinate operation may be used for one or more of the coordinate operation steps mentioned above, if the inverse coordinate operation is uniquely defined by the forward coordinate operation method. Public attributes: 4 attributes (coordinate operation name, coordinate operation alias, coordinate operation identifier and coordinate operation remarks) inherited from IO_IdentifiedObject and IO_IdentifiedObjectBase (see Tables 1 and 2), plus: |
| Attribute name | UML identifier | Data type | Obligation | Maximum Occurrence | Attribute description |
| Coordinate operation version | operationVersion | CharacterString | C | 1 | Version of the coordinate transformation (i.e. instantiation due to the stochastic nature of the parameters). Mandatory when describing a coordinate transformation, and should not be supplied for a coordinate conversion. |
| Coordinate operation validity | domainOfValidity | EX_Extent | O | 1 | Area or region or time frame in which this coordinate operation is valid. |
| Coordinate operation scope | scope | CharacterString | M | N | Description of usage, or limitations of usage, for which this coordinate operation is valid. If unknown, enter “not known”. |
| Coordinate operation accuracy | coordinateOperationAccuracy | DQ_Positional Accuracy | O | N | Estimate(s) of the impact of this coordinate operation on point accuracy. Gives position error estimates for target coordinates of this coordinate operation, assuming no errors in source coordinates. |

Table 49 — Defining elements of CC_Formula class

| Description: Specification of the coordinate operation method formula. |
| --- |
| Stereotype: Union Inheritance from: (none) Association roles: (none) Used by: CC_OperationMethod Public attributes: |
| Attribute name | UML identifier | Data type | Obligation | Maximum Occurrence | Attribute description |
| Coordinate operation method formula | formula | CharacterString | C | 1 | Formula(s) or procedure used by this operation method. |
| Coordinate operation method formula citation | formulaCitation | CI_Citation | C | 1 | Reference to a publication giving the formula(s) or procedure used by the coordinate operation method. |
| Condition: One and only one of the listed attributes shall be supplied. |

Edit Figures 5 through 12 in OGC 08-015 as follows:

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: IO_IdentifiedObjectBase, IO_IdentifiedObject, SC_CRS, RS_Identifier, CS_CoordinateSystem, CD_Datum, CC_CoordinateOperation, and CC_GeneralOperationParameter.

Figure 5 — IO_IdentifiedObject package

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: IO_IdentifiedObjectBase, GM_Object, SC_CRS, CC_CoordinateOperation, CD_Datum, CS_CoordinateSystem, SC_SingleCRS, and SC_GeneralDerivedCRS.

Figure 6 — SC_CoordinateReferenceSystem package

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: IO_IdentifiedObject and CS_CoordinateSystem.

Figure 7 — CS_CoordinateSystem package

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: SC_SingleCRS, CS_CoordinateSystem, and SC_GeneralDerivedCRS.

Figure 8 — Coordinate System type associations with Coordinate Reference System type

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: SC_SingleCRS, IO_IdentifiedObject, and CD_Datum.

Figure 9 — CD_Datum package

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: SC_SingleCRS, CD_Datum, and SC_GeneralDerivedCRS.

Figure 10 — Datum type associations with Coordinate Reference System type

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: IO_IdentifiedObject, SC_CRS, CC_CoordinateOperation, SC_SingleOperation, and SC_GeneralDerivedCRS.

Figure 11 — CC_CoordinateOperation package part 1

NOTE 	Although the class names are not in italics, the following classes shown above are abstract: IO_IdentifiedObject, CC_GeneralParameterValue, and CC_GeneralOperationParameter.

Figure 12 — CC_CoordinateOperation package part 2

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.