Open Geospatial Consortium	OGC Doc 08-158

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | GML 3.2.1 | CR | ? | ( rev | - | ( Current version: | 3.2.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec |  | Recom. Paper |  | Other | X |
| Title: ( | Extend GML Coordinate reference system schemas to include ISO 19111-2 Parametric CRS |
| Source: ( | Andrew Woolf (Natural Environment Research Council) |
| Work item code: ( |  |  | Date: ( | 2008-09-23 |
| Category: ( | B |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | ISO 19111-2 has extended the scope of ISO 19111 coordinate reference systems to include ‘parametric coordinate reference systems’ often used in environmental science communities. |
| Summary of change: ( | Add to GML implementations of ISO 19111-2 classes: SC_ParametricCRS, CS_ParametricCS, CD_ParametricDatum. |
| Consequences if ( not approved: | GML will be unable to encode important coordinate reference systems used for environmental data exchange, despite that standards-based conceptual models for these systems may be described using ISO 19111-2. |
| Clauses affected: ( |  |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Recommendation Papers |  |
| Other comments: ( | May need to update also 12.1.2 and D2.7 describing relationship with ISO 19111 (to include relationship with ISO 19111-2), and add references to ISO 19111-2 more generally (e.g. in 12.1.3). Also will need to add definitions to ‘Terms and definitions’ from ISO 19111-2: parametric coordinate system, parametric coordinate reference system. parametric datum, spatio-parametric coordinate reference system, spatio-parametric-temporal coordinate reference system. |

Additional clauses inserted, as below:

12.3.3.37 ParametricCRS

<element name="ParametricCRS" type="gml:ParametricCRSType" substitutionGroup="gml:AbstractSingleCRS"/>

<complexType name="ParametricCRSType">

<complexContent>

<extension base="gml:ParametricCRSType">

<sequence>

<element ref="gml:parametricCS"/>

<element ref="gml:parametricDatum"/>

</sequence>

</extension>

</complexContent>

</complexType>

gml:ParametricCRS is a 1D coordinate reference system where a physical or material property or function is used as the dimension. The parameter may be measured or be a function defined in other contexts, but in parametric coordinate systems it forms the coordinate system axis. Its relationship with a spatial dimension will usually be complex and non-linear. Parametric coordinate reference systems are frequently used in the environmental sciences.

EXAMPLES Pressure in meteorological applications; density (isopycnals) in oceanographic applications.

12.3.3.38 parametricCS

<element name="parametricCS" type="gml:ParametricCSPropertyType"/>

gml:parametyricCS is an association role to the parametric coordinate system used by this CRS.

12.3.3.39 parametricDatum

<element name="parametricDatum" type="gml:ParametricDatumPropertyType"/>

gml:parametricDatum is an association role to the parametric datum used by this CRS.

12.3.3.40 ParametricCRSPropertyType

<complexType name="ParametricCRSPropertyType">

<sequence minOccurs="0">

<element ref="gml:parametricCRS"/>

</sequence>

<attributeGroup ref="gml:AssociationAttributeGroup"/>

</complexType>

gml:ParametricCRSPropertyType is a property type for association roles to a parametric coordinate reference system, either referencing or containing the definition of that reference system.

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the more recent version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.opengeospatial.org.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, Recom. Paper = Recommendation Paper, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the TC Policies and Procedures".

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.