Open Geospatial Consortium	Document OGC 08-208

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | SensorML | CR | ? | ( rev | - | ( Current version: | 1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | SensorML change request - Make correct GML application schema |
| Source: ( | Arliss Whiteside |
| Work item code: ( |  |  | Date: ( | 2008-12-29 |
| Category: ( | F |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | SensorML 1.0 states that it is a GML Application Schema, but it does not meet all the requirements for a GML Application Schema. In particular, it frequently deviates from the required GML Object-property encoding. |
| Summary of change: ( | Improve SensorML 1.0 to meet all the requirements for a GML Application Schema, including the required GML Object-property encoding. |
| Consequences if ( not approved: | Since SensorML is not a correct GML Application Schema, extra work is required to use it, and some persons will not consider using it with GML. |
| Clauses affected: ( |  |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( |  |
| Other comments: ( | This change request references specific elements in GML 3.2.1. The corresponding elements in GML 3.1.1 sometimes have different element names. |
| Status ( |  |
| Disposition ( |  |

Place all XML elements encoding GML Objects in a substitutionGroup

In a GML Application Schema, all XML elements are either GML “Objects” or GML “properties”.  All GML Object XML elements are required to be in the substitutionGroup tree that is rooted in gml:AbstractObject.  That requires that the XML elements encoding objects to have public element names, which are always capitalized.

When no other existing GML Object would be a suitable substitutionGroup for a new GML Object, that Object is placed in the gml:AbstractGML substitutionGroup if the object may have an identity so that it can be used multiple times.  Such an Object with identity can and should use the required gml:id attribute, and it often should use some of the (optional) other properties in gml:AbstractGML, namely gml:identifier, gml:name, gml:description, gml:descriptionReference, and gml:metaDataProperty.  Otherwise, a new GML Object that is only used once is placed (directly) in the gml:AbstractObject substitutionGroup.

The following table lists the XML elements in all sensorML 1.0.1 XML Schema Documents that appear to encode GML Objects but are not currently in a substitutionGroup.

| XML Schema Document | XML Element Name | Should Place In substitutionGroup | Should Also Change |
| --- | --- | --- | --- |
| base.xsd | sml:Security | gml:AbstractObject |  |
|  | sml:Rights | gml:AbstractGML | Inherit gml:id |
|  | KeywordList | gml:AbstractGML | Inherit gml:id Make name public |
|  | IdentifierList | gml:AbstractGML | Use gml:id Make name public |
|  | ClassifierList | gml:AbstractGML | Use gml:id Make name public |
|  | sml:Term | gml:AbstractGML | Inherit gml:descriptionReference Use gml:CodeType for “value” |
|  | sml:ContactList | gml:AbstractGML | Inherit gml:id and gml:Description |
|  | sml:Person | gml:AbstractGML | Inherit gml:id |
|  | sml:ResponsibleParty | gml:AbstractGML | Inherit gml:id |
|  | sml:contactInfo | gml:AbstractObject | Add new sml:ContactInfo object |
|  | sml:phone | gml:AbstractObject | Add new sml:Phone object |
|  | sml:address | gml:AbstractObject | Add new sml:Address object |
|  | sml:Document | gml:AbstractGML | Inherit gml:id |
|  | sml:DocumentList | gml:AbstractGML | Inherit gml:id |
|  | sml:EventList | gml:AbstractGML | Inherit gml:id |
|  | sml:Event | gml:AbstractGML | Inherit gml:id |
| method.xsd | sml:ProcessMethod | gml:AbstractGML |  |
|  | RulesDefinition | gml:AbstractGML | Inherit gml:description Make name public |
|  | AlgorithmDefinition | gml:AbstractGML | Inherit gml:description Make name public |
|  | ImplementationCode | gml:AbstractGML | Inherit gml:description Make name public |
|  | sml:ruleLanguage | gml:AbstractObject | Add new sml:AbstractRules object |
|  | sml:schematron | gml:AbstractObject | Add new sml:SchematronRules object |
|  | sml:relaxNG | gml:AbstractObject | Add new sml:RelaxNGRules object |
| process.xsd | sml:_Process | gml:AbstractGML | Change name to sml:AbstractProcess |
|  | InputList | gml:AbstractGML | Use gml:id Make name public |
|  | OutputList | gml:AbstractGML | Use gml:id Make name public |
|  | ParameterList | gml:AbstractGML | Use gml:id Make name public |
|  | ComponentList | gml:AbstractGML | Use gml:id Make name public |
|  | ConnectionList | gml:AbstractGML | Use gml:id Make name public |
|  | sml:connection | gml:AbstractGML | Use gml:identifier or gml:name Capitalize element name |
|  | sml:Link | gml:AbstractObject |  |
|  | sml:ArrayLink | gml:AbstractObject |  |
| sensorML.xsd | sml:SensorML | gml:AbstractObject? |  |
| system.xsd | PositionList | gml:AbstractGML | Use gml:id Make name public |
|  | InterfaceList | gml:AbstractGML | Use gml:id Make name public |
|  | sml:InterfaceDefinition | gml:AbstractGML | Inherit gml:id |
|  | ParameterList | sml:AbstractList | Make name public |

The following table lists the XML elements in all sweCommon 1.0.1 XML Schema Documents that appear to encode GML Objects but are not currently in a substitutionGroup.

| XML Schema Document | XML Element Name | Should Place In substitutionGroup | Should Also Change |
| --- | --- | --- | --- |
| aggregateTypes.xsd | swe:AbstractDataRecord | gml:AbstractGML | Inherit gml:name |
|  | swe:AbstractDataArray | gml:AbstractObject |  |
| basicTypes.xsd | swe:Interval | gml:AbstractObject |  |
| curveTypes.xsd | (none) |  |  |
| data.xsd | swe:DataBlockDefinition | gml:AbstractGML | Inherit gml:id |
|  | swe:DataStreamDefinition | gml:AbstractGML | Inherit gml:id |
| encoding.xsd | swe:StandardFormat | gml:AbstractGML | Inherit gml:id |
|  | swe:TextBlock | gml:AbstractGML | Inherit gml:id |
|  | swe:BinaryBlock | gml:AbstractObject |  |
|  | Component | gml:AbstractObject | Make name public |
|  | Block | gml:AbstractObject | Make name public |
|  | swe:MultiplexedStream-Format | gml:AbstractGML | Inherit gml:id |
|  | swe:XMLBlock | gml:AbstractGML | Inherit gml:id |
| phenomenon.xsd | (none) |  |  |
| positionTypes.xsd | (none) |  |  |
| simpleTypes.xsd | swe:Boolean | gml:AbstractGML | Omit swe:SimpleComponent-AttributeGroup |
|  | swe:Quantity | gml:AbstractGML |  |
|  | swe:QuantityRange | gml:AbstractGML |  |
|  | swe:Count | gml:AbstractGML | Omit swe:SimpleComponent-AttributeGroup |
|  | swe:CountRange | gml:AbstractGML | Omit swe:SimpleComponent-AttributeGroup |
|  | swe:Category | gml:AbstractGML | Omit swe:SimpleComponent-AttributeGroup |
|  | swe:Time | gml:AbstractGML |  |
|  | swe:TimeRange | gml:AbstractGML |  |
|  | swe:Text | gml:AbstractGML |  |
|  | swe:ObservableProperty | gml:AbstractGML |  |
|  | swe:AllowedValues | gml:AbstractGML | Inherit gml:id |
|  | swe:AllowedTokens | gml:AbstractGML | Inherit gml:id |
|  | swe:AllowedTimes | gml:AbstractGML | Inherit gml:id |
| swe.xsd | (none) |  |  |
| temporalAggregates.xsd | (none) |  |  |
| xmlData.xsd | swe:Item | gml:AbstractObject |  |
|  | swe:Record | gml:AbstractObject |  |
|  | swe:Array | gml:AbstractObject |  |

Make all XML elements encoding complex GML properties use a complexType with name ending in “PropertyType”

In a GML Application Schema, all XML elements are either GML “Objects” or GML “properties”.  GML properties with simple contents are directly encoded as XML elements, usually using xsd:simpleType.  Each GML property with more complex contents is encoded as an XML element that should use a globally-named xsd:complexType with a name of the form “XxxxPropertyType”.  The “Xxxx” is that name of the associated GML Object which contains the desired complex property contents.  Complex GML property XML elements are rarely in a substitutionGroup, and shall NOT be in the substitutionGroup tree rooted in gml:AbstractObject.

The following table lists the XML elements in all sensorML 1.0.1 XML Schema Documents that appear to encode complex GML “properties” but do not currently use a globally named complexType with a name of the form “XxxxPropertyType”.

| XML Schema Document | XML Element Name | Should Use Type | Should Also |
| --- | --- | --- | --- |
| base.xsd | sml:securityConstraint | sml:SecurityPropertyType |  |
|  | sml:validTime | sml:TimeInstantOrPeriod-PropertyType |  |
|  | sml:legalConstraint | sml:RightsPropertyType |  |
|  | sml:keywords | sml:KeywordListProperty-Type |  |
|  | sml:identification | sml:IdentifierListProperty-Type |  |
|  | identifier (in sml:identification) | sml:TermPropertyType | Omit “name” attribute by using xlink:title instead |
|  | sml:classification | sml:ClassifierListProperty-Type |  |
|  | classifier (in sml:classification) | sml:TermPropertyType-PropertyType | Omit “name” attribute by using xlink:title instead |
|  | sml:contact | sml:ContactOrListProperty- Type |  |
|  | member (in sml:ContactList | sml:ContactPropertyType | Change “member” to “contact” |
|  | sml:contactInfo | sml:ContactInfoPropertyType | Change property to include new sml:ContactInfo object |
|  | sml:phone | sml:PhonePropertyType | Change property to include new sml:Phone object |
|  | sml:address | sml:AddressPropertyType | Change property to include new sml:Address object |
|  | sml:documentation | sml:DocumentOrListProperty-Type |  |
| base.xsd (continued) | member (in sml:DocumentList | sml:DocumentPropertyType | Change “member” to “document” Omit “name” attribute by using xlink:title instead |
|  | sml:history | sml:EventListPropertyType | Omit “history” group, instead directly using sml:history |
|  | member (in EventList) | sml:EventPropertyType | Change “member” to “event” Omit “name” attribute by using xlink:title instead |
|  | sml:capabilities | swe:DataRecordPropertyType | Omit “name” attribute by using xlink:title instead |
|  | sml:characteristics | swe:DataRecordPropertyType | Omit “name” attribute by using xlink:title instead |
| method.xsd | rules (in ProcessMethodType) | swe:RulesDefinitionProperty-Type | Change property to include new sml:RulesDefinition object |
|  | algorithm (in ProcessMethodType) | sml:AlgorithmDefinition-PropertyType | Change property to include new sml:AlgorithmDefinition object |
|  | sml:methodProperty-Type | sml:ProcessMethodProperty-Type | Change name of this complexType |
|  | sml:ruleLanguage | sml:RulesPropertyType | Change property to include new sml:Rules object, and change “rulesLanguage” to “rules” |
| process.xsd | sml:inputs | sml:InputListPropertyType |  |
|  | sml:outputs | sml:OutputListPropertyType |  |
|  | sml:parameters | sml:ParameterListProperty-Type |  |
|  | component (in sml:Components) | sml:ProcessPropertyType | Omit “name” attribute by using xlink:title instead Consider changing property name to “process” |
|  | dataDefinition (in sml:DataSourceType | sml:DataDefinitionProperty-Type |  |
|  | values (in sml:DataSourceType | sml:ValuesPropertyType? | Consider improving property name “values” |
|  | observationReference (in sml:DataSourceType | sml:ObservationProperty-Type? | Consider changing property name to “observation” |
|  | sml:connections | sml:ConnectionListProperty-Type |  |
|  | sml:connection | sml:LinkPropertyType | Omit “name” attribute? |
|  | sml:inputsPropertyType | sml:InputsPropertyType | Capitalize property type name |
|  | sml:outputsPropertyType | sml:OutputsPropertyType | Capitalize property type name |
| process.xsd (continued) | sml:parameters-PropertyType | sml:ParametersPropertyType | Capitalize property type name |
|  | sml:components-PropertyType | sml:ComponentsProperty-Type | Capitalize property type name |
|  | sml:dataSources-PropertyType | sml:DataSourcesProperty-Type | Capitalize property type name |
|  | sml:connections-PropertyType | sml:ConnectionsProperty-Type | Capitalize property type name |
|  | sml:IoComponent-PropertyType | sml:IoComponent-PropertyType | Omit “name” attribute by using xlink:title instead |
| sensorML.xsd | member (in sml:SensorML) | sml:SMLmemberProperty-Type |  |
| system.xsd | sml:spatialReference-Frame | sml:EngineeringCRS-PropertyType |  |
|  | sml:temporal-ReferenceFrame | sml:TemporalCRSProperty-Type |  |
|  | sml:location | sml:PointOrCurveProperty-Type |  |
|  | sml:position | sml:PositionPropertyType | Omit “name” attribute by using xlink:title instead |
|  | sml:timePosition | sml:TimePropertyType | Omit “name” attribute by using xlink:title instead |
|  | sml:positions | sml:PositionListProperty-Type | Change property to include new sml:PositionList object |
|  | sml:interfaces | sml:InterfaceListProperty-Type | Change property to include new sml:InterfaceList object |
|  | sml:interface | sml:InterfaceDefinition-PropertyType | Change property to include new sml:InterfaceDefinition object Omit “name” attribute by using xlink:title instead |
|  | parameters (in sml:ComponentArrayType | sml:ComponentParameters-PropertyType |  |

The following table lists the XML elements in all sweCommon 1.0.1 XML Schema Documents that appear to encode complex GML “properties” but do not currently use a globally named complexType with a name of the form “XxxxPropertyType”.

| XML Schema Document | XML Element Name | Should Use Type | Should Also |
| --- | --- | --- | --- |
| aggregateTypes.xsd | swe:Count | swe:CountPropertyType | Change Object to property |
|  | elementCount (in AbstractDataArrayType) | swe:CountPropertyType |  |
|  | case (in ConditionalDataType | swe:ConditionalValue-PropertyType | Omit “name” attribute by using xlink:title instead |
|  | condition (in AbstractConditionalType) | swe:AnyDataProperty-Type? | Omit “name” attribute by using xlink:title instead |
|  | data (in ConditionalValueType) | swe:AnyDataProperty-Type? |  |
| basicTypes.xsd | (none) |  |  |
| curveTypes.xsd | (none) |  |  |
| data.xsd | (none) |  |  |
| encoding.xsd | (none) |  |  |
| phenomenon.xsd | (none) |  |  |
| positionTypes.xsd | (none) |  |  |
| simpleTypes.xsd | (none) |  |  |
| swe.xsd | (none) |  |  |
| temporalAggregates.xsd | swe:TimeGridPropertyType | Should include swe:TimeGrid instead of swe:TimeInstantGrid |  |
| xmlData.xsd | (none) |  |  |

Include documentation of meaning in all GML Objects and properties

I think the definitions of all XML encodings of GML Objects should include a <documentation> element which provides the meaning or use of that Object.  Similarly, all XML encodings of simple properties should include a <documentation> element which provides the meaning or use of that property.  With some exceptions, most definitions of XML encodings of GML Objects and of simple GML properties in sensorML 1.0.1 and sweCommon 1.0.1 do not include any documentation of meaning or use.

Similarly, I think the definitions of all XML encodings of complex GML properties should include a <documentation> element which specifies that either the optional Object or the optional reference to such an Object shall be included.  If both may be included, that should be explicitly stated, together with the meaning when both are included.  With some exceptions, most definitions of XML encodings of complex GML properties in sensorML 1.0.1 and sweCommon 1.0.1 do not include any documentation of the limitations or meaning of the optional components.

Use or adapt GML elements with similar meanings or uses

A GML Application Schema should use or adapt the element, attribute, and type items which are already defined in GML for any needed item with essentially the same meaning or use.  Such adaptation may include extending or restricting the item contents.  Such adaptation may also include using another item name (to better indicate the semantics).

In the current absence of documentation of the meanings or uses of many items defined in sensorML 1.0.1 and sweCommon 1.0.1, it is hard to determine which items defined there are similar to items already defined in GML.  Nevertheless, it appears that a significant number of the defined items are similar to elements already defined in GML.

The following table lists the XML items defined in all sensorML 1.0.1 XML Schema Documents that appear to have essentially the same meaning or use as a corresponding item in GML.

| XML Schema Document | XML Item Name | Should Use Or Adapt GML Item Named | In GML XML Schema Document |
| --- | --- | --- | --- |
| base.xsd | sml:AbstractSMLType | gml:DefinitionType | dictionary.xsd |
|  | name (in swe:identification) | gml:name | gmlBase.xsd |
|  | id (in swe:identification) | gml:id | gmlBase.xsd |
|  | name (in swe:classification) | gml:name | gmlBase.xsd |
|  | id (in swe:classification) | gml:id | gmlBase.xsd |
|  | definition (in sml:Term) | gml:descriptionReference | gmlBase.xsd |
| method.xsd | (none) |  |  |
| process.xsd | sml:AbstractProcessType | gml:DefinitionType | dictionary.xsd |
|  | id (in swe:inputs) | gml:id | gmlBase.xsd |
|  | id (in swe:outputs) | gml:id | gmlBase.xsd |
|  | id (in swe:parameters) | gml:id | gmlBase.xsd |
|  | id (in swe:AbstractListType) | gml:id | gmlBase.xsd |
| sensorML.xsd | sml:SensorML | gml:Dictionary | dictionary.xsd |
| system.xsd | id (in swe:positions) | gml:id | gmlBase.xsd |
|  | id (in swe:interfaces) | gml:id | gmlBase.xsd |

The following table lists the XML items defined in all sweCommon 1.0.1 XML Schema Documents that appear to have essentially the same meaning or use as a corresponding item in GML.

| XML Schema Document | XML Item Name | Should Use Or Adapt GML Item Named | In GML XML Schema Document |
| --- | --- | --- | --- |
| aggregateTypes.xsd | name (in ConditionalDataType) | xlink:title | xlinks.xsd |
|  | name (in AbstractConditionalType) | xlink:title | xlinks.xsd |
|  | name (in DataComponent-PropertyType) | xlink:title | xlinks.xsd |
| basicTypes.xsd | swe:UomSymbol | gml:UomSymbol | basicTypes.xsd |
|  | swe:UomURI | gml:UomURI | basicTypes.xsd |
|  | swe:UomIdentifier | gml:UomIdentifier | basicTypes.xsd |
|  | swe:CodeSpaceProperty-Type | xsd:anyURI |  |
|  | swe:ScopedNameType | gml:CodeType | basicTypes.xsd |
|  | swe:decimalList | gml:doubleList | basicTypes.xsd |
|  | swe:countList | gml:integerList | basicTypes.xsd |
|  | swe:tokenList | gml:NCName (?) | basicTypes.xsd |
|  | swe:Interval | gml:Envelope (?) | geometryBasic0d1d.xsd |
| curveTypes.xsd | (none identified) |  |  |
| data.xsd | (none identified) |  |  |
| encoding.xsd | (none identified) |  |  |
| phenomenon.xsd | swe:PhenomenonType | gml:DefinitionType | dictionary.xsd |
| positionTypes.xsd | swe:Envelope | gml: EnvelopeWithTimePeriod | feature.xsd |
|  | swe:EnvelopeType | gml:EnvelopeWithTime-PeriodType | feature.xsd |
|  | swe:Vector | gml:vector | geometryBasic0d1d.xsd |
|  | swe:VectorType | gml:VectorType | geometryBasic0d1d.xsd |
| simpleTypes.xsd | swe:definition | gml:descriptionReference | gmlBase.xsd |
|  | swe:Boolean | gml:Boolean | valueObjects.xsd |
|  | swe:Quantity | gml:Quantity | valueObjects.xsd |
|  | swe:QuantityRange | gml:QuantityExtent | valueObjects.xsd |
|  | swe:Count | gml:integerOrNilReason | basicTypes.xsd |
|  | swe:CountRange | gml:CountExtent | valueObjects.xsd |
|  | swe:Category | gml:Category | valueObjects.xsd |
|  | swe:AllowedValues | gml:QuantityExtent | valueObjects.xsd |
| swe.xsd | (none identified) |  |  |
| temporalAggregates.xsd | (none identified) |  |  |
| xmlData.xsd | swe:Item | gml:AbstractObject | gmlBase.xsd |
|  | swe:Array | gml:ValueArray | valueObjects.xsd |

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the more recent version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.opengeospatial.org.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, BPD – Best Practices Document, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specification or best practices documents that are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.