Open Geospatial Consortium	Document OGC 09-040

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | SensorML | CR | ? | ( rev | - | ( Current version: | 1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | x | Best Practices Paper |  | Other |  |
| Title: ( | SensorML change request - Harmonize with ISO 19115-2 and ISO 19130 |
| Source: ( | Simon Cox |
| Work item code: ( |  |  | Date: ( | 2009-03-25 |
| Category: ( | C | (Changes functional names) |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) |  |
| Reason for change: ( | The scope of SensorML overlaps significantly with elements from ISO 19115-2 and ISO 19130. SensorML could be understood as an implementation of concepts from these standards. This needs to be made explicit within the SensorML document. Furthermore, the analysis in ISO 19115-2 provides clear separation, in the class model; on the one hand between (a) sensors and instruments (whose input is a physical stimulus) and (b) algorithms and processing steps (whose inputs are measures derived from a previous step or sensor); and on the other between (c) generic sensors and algorithms or types, and (d) instances of their application. In contrast, in SensorML these distinctions are hidden inside the Process class, by selection amongst the optional properties and the type chosen for their values. Within SensorML specialization is based on a very different analysis. The compatibility between these analyses should be considered carefully, and harmonization attempted if possible. N.B. the ISO 19115-2 classes do not have the detail provided in SensorML, but can be seen as generic parents that can be extended and specialized. For example, some of the classes in ISO 19130 are specializations of ISO 19115-2 classes. |
| Summary of change: ( | Provide an explanation of how certain classes in ISO 19115-2 and ISO 19130 are implemented by SensorML, in particular: LI_Lineage, LE_ProcessStep, LE_Processing, LE_Algorithm MI_Operation, MI_Event, MI_Instrument SD_Sensor, SD_SensorParameters, SD_SensorModel N.B. MI_Event appears to be related to O&M Observation. |
| Consequences if ( not approved: | Difficult/impossible to integrate SensorML into implementations of models designed using the ISO UML Harmonized Model. |
| Clauses affected: ( | Most |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( |  |
| Other comments: ( |  |
| Status ( |  |
| Disposition ( |  |

# Comments

Enter the AS or Implementation Specification Name and Number in this box. For example, WMS 1.1.1 or GML 3.0. Do not prefix the number with anything, i.e. do not use "OGC", "GSM" or "OGC" etc.

Enter the CR number here. This number is allocated by the OGC support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the more recent version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.opengeospatial.org.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X. AS = Abstract Specification, IS = Implementation Specification, BPD – Best Practices Document, Other = DIPR/IPR, etc.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or more OGC members or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

IF there is one, enter the work item code or issue code that is applicable to the change. These codes will relate to Work Items identified in a WBS associated with a particular OGC initiative. If there is no code, leave blank.

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

If known, list here the specification or best practices documents that are affected or the CRs which are linked.

Explanation of Field: If there is associated documentation, such as an lengthy change request or new text for consideration, please reference the OGC document number and document title.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is the status of the change request. For a new submission, please enter “NEW”. Other options as the change request is processed are: Assigned, Verified, Resolved, and Closed.

This field is used to assign the RWG decision for this Change Request. Options include: Deferred, Accepted, and Rejected.