| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | WPS 1.0.0 | CR | ? | ( rev | -1- | ( Current version: | 1.0.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | AS |  | Imp Spec | X | Best Practices Paper |  | Other |  |
| Title: ( | Web Processing Service Change Request – a standardised method for querying the status of asynchronous process |
| Source: ( | Science and Technology Facilities Council (STFC) |
| Work item code: ( |  |  | Date: ( | 29 July 2009 |
| Category: ( | B |  |  |
|  | Use one of the following categories: F (Critical correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in the TC Policies and Procedures. |  |
| Reason for change: ( | The WPS 1.0.0 specification does not provide any mechanism for querying the status of an asynchronous process, though the specification does require an ExecuteResponse document for an asynchronous process to contain a “statusLocation” attribute for indicating the status URL for the process. This often leads to ad-hoc approaches to implementing a suitable function for checking the status of asynchronous processes through standardised WPS. Hence, it results in non-interoperability between WPS clients, SOAP-based workflows in particular that have the need to submit an asynchronous process for execution, check its status for completion and retrieve the final output through a standardised WPS in an automated way. |
| Summary of change: ( | A mechanism for querying the status of asynchronous process |
| Consequences if ( not approved: | Non-interoperability between WPS clients, particularly SOAP-based workflows |
| Clauses affected: ( |  |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Abstract specifications |  |
|  |  | Best Practices Document |  |
| Supporting Doc. ( |  |
| Other comments: ( |  |
| Status ( |  |
| Disposition ( |  |

Change 1: “GetStatus” Operation

1. Definition

GetStatus operation enables checking the status of a WPS asynchronous process that has been submitted to the WPS server for execution. This operation should only be applicable to the asynchronous processes that support this operation (i.e. statusSupported set to True in the DescribeProcess response for the process).

2. GetStatus Request Parameters

We propose that a request to check the status of a process should include the parameters listed and defined in Table 1 below:

| Name | Definition | Data Type and Value | Multiplicity and Use |
| --- | --- | --- | --- |
| ProcessIdentifier | Unique identifier assigned to a specific instance of an asynchronous process by the server and included in the Execute response of the process as value of the “statusLocation” attribute. | Character String type. Could also be ows:CodeType, as adaptation of MD_Identifier in ISO 19115. Value is process identifier indicated in Execute Response document. | One (Mandatory) |
| Request | Operation name | Character String type, not empty Value is operation name, namely, “GetStatus” | One (Mandatory) |
| Service | Service type identifier | Character String type, not empty Value is OWS type abbreviation, namely ―WPS | One (Mandatory) |
| Version | Specification version for operation | Character String type, not empty Value is specified by each Implementation Specification and Schemas version | One (Mandatory) |

Table 1:  “GetStatus” Request Parameters

3. Example “GetStatus” Requests

Example GET “GetStatus” request:

http://foo.bar.1/wps?version=1.0.0&request=GetStatus&service=WPS&ProcessIdentifier=cb1557397169547d63c2d1388e8dd810

Example POST “GetStatus” Process Request:

<?xml version="1.0" encoding="UTF-8"?>

<GetStatus xmlns="http://www.opengis.net/wps/1.0.0" xmlns:ows="http://www.opengis.net/ows/1.1" xmlns:xlink="http://www.w3.org/1999/xlink" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.opengis.net/wps/1.0.0 ../wpsGetStatus_request.xsd" service="WPS" version="1.0.0" language="en-CA">

<ows:Identifier> cb1557397169547d63c2d1388e8dd810</ows:Identifier>

</GetStatus>

4. “GetStatus” Operation Response

The response to a successful GetStatus operation should be a standard WPS ExecuteResponse document with the “wps:Status” element indicating the most recent status of the process in question (highlighted in yellow in the example below).

Example WPS response:

<?xml version="1.0" encoding="UTF-8"?>

<wps:ExecuteResponse xmlns:wps=http://www.opengis.net/wps/1.0.0......statusLocation="cb1557397169547d63c2d1388e8dd810" xsi:schemaLocation="http://www.opengis.net/wps/1.0.0 http://schemas.opengis.net/wps/1.0.0/wpsExecute_response.xsd">

<wps:Process wps:processVersion="1.0">

<ows:Identifier>RunTraj</ows:Identifier>

<ows:Title>BADC Trajectory Service</ows:Title>

</wps:Process>

<wps:Status creationTime="2009-05-29T13:00:03.0Z">

<wps:ProcessStarted/>

</wps:Status>

<wps:ProcessOutputs>

<wps:Output>

<ows:Identifier>RunTraj</ows:Identifier>

<ows:Title>BADC Trajectory Service</ows:Title>

<ows:Abstract>The service provides a user friendly interface to an atmospheric trajectory model.</ows:Abstract>

<wps:Reference href="http://glue.badc.rl.ac.uk/wps-jsdl/services/dl?job_id=cb1557397169547d63c2d1388e8dd810&amp;file_name=traj_output.xml"/>

</wps:Output>

</wps:ProcessOutputs>

</wps:ExecuteResponse>

Attempts to query the status of a process that doesn’t support “GetStatus” operation should throw an appropriate OWS Exception as below:

<?xml version="1.0" encoding="UTF-8"?>

<ExceptionReport xmlns="http://www.opengis.net/ows/1.1"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.opengis.net/ows/1.1 ../owsExceptionReport.xsd"

version="1.0.0" xml:lang="en">

<Exception exceptionCode="InvalidOperation">

<ExceptionText>”GetStatus” is not a valid operation for this process</ExceptionText>

</Exception>

</ExceptionReport>