Open Geospatial Consortium

Technology Office

4899 North Old State Road 37
Bloomington, IN 47408

Telephone: +1-812-334-0601
Facsimile: +1-812-961-2053

Request For Quotation

And

Call For Participation

In the

Federal Aviation Administration (FAA) Special activity Airspace (SAA) Dissemination Pilot

(FAA SAA Dissemination Pilot)

Appendix C to Annex B – SR Web Service Description Document (WSSD)

RFQ Issuance Date: September 20, 2010

Proposal Due Date: October 18, 2008

U.S. Department of Transportation

Federal Aviation Administration

Web Service Description Document

Aeronautical Information Management

Special Activity Airspace Management Static Repository Service

Version 0.3

August 16, 2010

Web Service Description Document

Approval Signature Page

Aeronautical Information Management

Special Activity Airspace Management

Static Repository Service

| Approval Signatures |
| --- |
| Participant | Name | Signature | Date Signed |

| REVISION RECORD |
| --- |
| Revision Letter | Description | Date | Entered By |
| Version 0.1 | Initial Draft | May 28, 2010 | Kevin Lew |
| Version 0.2 | Addressed internal comments. | June 1, 2010 | Kevin Lew |
| Version 0.3 | Addressed comments from SWIM, the Static Repository Developers, and ERAM | August 16, 2010 | Kevin Lew |

Table of Contents

1.	Scope	5

1.1	Background	5

2.	Applicable Documents	6

2.1	Government Documents	6

2.2	Non-Government Stands and Other Publications	8

3.	Definitions	9

3.1	Abbreviations and Acronyms	9

4.	Web Services Properties and Capabilities	10

4.1	Service Profile	10

4.1.1	Service Provider	10

4.1.2	Service Consumers	10

4.1.3	Service Functionality	11

4.1.4	Security	11

4.1.5	Quality of Service	11

4.1.6	WSDL Documents	11

4.2	Service Interfaces	12

4.2.1	Types	12

4.2.2	Messages	17

4.2.3	Operations	18

4.2.4	Lists of Interfaces	21

4.3	Service Implementation	21

4.3.1	End Points	22

Appendix A.	Accepted Data Elements	24

List of Tables

TBL 4-1 SAA SR Service Quality of Service Parameters	12

TBL 4-2 SAA SR Put Service Data Elements	13

TBL 4-3 SAA SR Get Service Data Elements	15

TBL 4-4 SAA SR Put Service Message Descriptions	18

TBL 4-5 SAA SR Get Service Message Descriptions	18

TBL 4-6 SAA SR Get Service Message Descriptions	19

TBL 4-7 insertSaa Operation Description	19

TBL 4-8 updateSaa Operation Description	20

TBL 4-9 insertUnit Operation Description	20

TBL 4-10 getNewUuid Operation Description	20

TBL 4-11 getSaaByUuid Operation Description	20

TBL 4-12 getSaaNames Operation Description	21

TBL 4-13 getSaaUUID Operation Description	21

TBL 4-14 getUnits Operation Description	21

TBL 4-15 validateSaa Operation Description	22

TBL 4-16 List of Interfaces	22

TBL 4-17 SAA SR Put Service Quality of Service Parameters	23

TBL 4-18 SAA SR Service Quality of Service Parameters	24

TBL 4-19 SAA SR Notification Service Quality of Service Parameters	24

# Scope

This Web Service Description Document (WSDD) was prepared in accordance with Federal Aviation Administration (FAA) Standard FAA-STD-065.  It provides the design characteristics for the interface between Special Activity Airspace (SAA) Static Repository (SR) Service and its web service clients.  This WSDD satisfies the interface design requirements for the Static Repository Service requirements documented in the Aeronautical Information Management (AIM) Special Activity Airspace Management Web Services Interface Requirements Document (IRD).

## Background

This document describes the interface between the AIM SAA SR Service and web service clients.

SAA is an unofficial term of convenience to collectively describe Special Use Airspace (SUA), Air Traffic Control Assigned Airspace (ATCAA), and other airspace that can be reserved for use.  The use of the term SAA in this document refers to SUAs and ATCAAs.

An SUA is a region of airspace designated to be used (typically by the military) based on a schedule.

An ATCAA is an airspace assigned by air traffic control to provide air traffic segregation between the specified activities being conducted within the assigned airspace and other Instrument Flight Rules (IFR) traffic.

The SAA SR maintains the static definitions of SAAs.  The static definition is a digital representation of the legal definition of the SAA using the Aeronautical Information Exchange Model (AIXM) specification.  The SAA SR Service is a System Wide Information Management (SWIM)-compliant web service that allows for the ability to update SAA static definitions as well as disseminate them to users of the service.

# Applicable Documents

## Government Documents

The following documents form a part of this WSDD to the extent specified herein.

| FAA SPECIFICATIONS: |
| --- |
| December 22, 2009 | System-Wide Information Management (SWIM) Service Specification Document (SvSD) Segment 1, version 1.7 |
|  | SWIM WS-I Basic Security Profile 1.1 |
| May 23, 2007 | System-Wide Information Management (SWIM) Final Program Requirements (FPR) Segment 1, Rev. 7.3 |
| FAA STANDARDS: |
| FAA-STD-063 May 1, 2009 | Standard Practice, XML Namespaces |
| FAA-STD-064 May 1, 2009 | Standard Practice, Web Service Registration |
| FAA-STD-065 February 26, 2010 | Standard Practice, Preparation of Web Service Description Documents |
| FAA-STD-066 February 26, 2010 | Standard Practice, Web Service Taxonomies |
| FAA-STD-025f November 30, 2007 | Preparation of Interface Documentation |
| STANDARDS FOR FAA SWIM PROGRAM COMPLIANCE: |
| IETF RFC 2616 June 1999 | Hypertext Transfer Protocol – HTTP/1.1 |
| W3C SOAP v. 1.2, Pt. 1 Recommendation April 27, 2007 | SOAP Version 1.2 Part 1: Messaging Framework (Second Edition) |
| W3C XML Recommendation September 29, 2006 | World Wide Web Consortium Extensible Markup Language (XML) version 1.0, fourth edition. |
| OASIS UDDI v. 3.0.2 October 19, 2004 | Universal Description, Discovery, and Integration (UDDI) Standard, version 3.0.2 |
| W3C WSDL v. 1.1 Note March 15, 2001 | World Wide Web Consortium Web Services Description Language (WSDL) version 1.1 |
| IETF RFC 2246 January 1999 | Transport Layer Security (TLS) – version 1.0 |
| IETF INTERNET-DRAFT November 18, 1996 | The Secure Sockets Layer (SSL) Protocol Version 3.0 |
| OTHER FAA PUBLICATIONS: |
| April 10, 2008 | JO 7400.2G – Procedures for Handling Airspace Matters |
| February 16, 2010 | JO 7400.8S – Special Use Airspace |
| March 9, 2009 | System Wide Information Management (SWIM) Governance Plan, Version 2.1 |
| June 23, 2010 | Aeronautical Information Management (AIM) Special Activity Airspace (SAA) Management Web Services Interface Requirements Document (IRD) version 1.0 https://swimwiki.tc.faa.gov/download/attachments/6881348/SWIM+Special+Activity+Airspace+Requirements.doc |

## Non-Government Standards and Other Publications

The following documents form a part of this WSDD to the extent specified herein.

| STANDARDS: |  |
| --- | --- |
| Aeronautical Information Exchange Model 5.0 Specification October 2008 | The model used for defining SAAs used in the transmission to and from the SAA SR Service. http://www.aixm.aero/public/standard_page/download_5_0.html |
| Internet Engineering Task Force (IETF) Request for Comments (RFC) 791 September 1981 | Internet Protocol (IP) as updated by RFC 1349 |
| IETF RFC 792 September 1, 1981 | Internet Control Message Protocol (ICMP), updated by RFC 950 |
| IETF RFC 793 September 1981 | Transmission Control Protocol (TCP), updated by RFC 3168 |
| IETF RFC 826 November 1, 1982 | Ethernet Address Resolution Protocol (ARP) |
| IETF INTERNET-DRAFT November 18, 1996 | The Secure Sockets Layer (SSL) Protocol Version 3.0 |
| IETF RFC 2460 December 1998 | Internet Protocol, Version 6 (IPv6) Specification |
| Web Services Security UsernameToken Profile 1.1 February 1, 2006 | Web Services Security UsernameToken Profile 1.1, OASIS Standard Specification http://docs.oasis-open.org/wss/v1.1/wss-v1.1-spec-os-UsernameTokenProfile.pdf |

# Definitions

SOAP - A protocol specification for exchanging structured information in the implementation of Web Services in computer networks.

## Abbreviations and Acronyms

AIM	Aeronautical Information Management

AIXM	Aeronautical Information Exchange Model

ARP	Address Resolution Protocol

ARTCC	Air Route Traffic Control Center

ATCAA	Air Traffic Control Assigned Airspace

ATM	Air Traffic Management

ERAM	En Route Automation Modernization

FAA	Federal Aviation Administration

FAA-STD	FAA Standard

GML	Geography Markup Language

HTTP	Hypertext Transfer Protocol

HTTPS	Hypertext Transfer Protocol over Secure Socket Layer

ICAO	International Civil Aviation Organization

ICMP	Internet Control Message Protocol

ID	Identifier

IETF	Internet Engineering Task Force

IP	Internet Protocol

IRD	Interface Requirements Document

JMS	Java Message Service

MEP	Message Exchange Pattern

MILOPS	Military Operations Systems

NAS	National Airspace System

OSI	Open System Interconnection

RFC	Request For Comments

SAA	Special Activity Airspace

SAA OR	Special Activity Airspace Operational Repository

SAA PR	Special Activity Airspace Project Repository

SAA SR	Special Activity Airspace Static Repository

SSL	Secure Socket Layer

STD	Standard

SUA	Special Use Airspace

SvSD	SWIM Services Specification Document

SWIM	System-Wide Information Management

TBD	To Be Determined

TCP	Transmission Control Protocol

TLS	Transport Layer Security

UDDI	Universal Description, Discovery, and Integration

UUID	Universally Unique Identifier

WSDD	Web Service Description Document

WSDL	Web Services Description Language

WS-I	Web Services Interoperability Organization

XML	Extensible Markup Language

# Web Services Properties and Capabilities

The SAA SR Service is a collection of three different web services:  the SAA SR Put Service, the SAA SR Get Service, and the SAA SR Notification Service.

The SAA Static Repository is populated through submissions of SAAs from the SAA Project Repository through calls to the SAA SR Put Service.  The web service handles either the insertion of a new SAA into the Static Repository or an update to an existing SAA.

The SAA SR Get Service provides operations for service consumers to call to retrieve data related to SAAs through request/response services.  These requests can include retrieving SAA definitions, Universally Unique Identifiers (UUID), names, as well as validating SAAs submitted by the service consumer.

The SAA SR Notification Service is a Java Message Service (JMS) publish/subscribe (pub/sub) service that provides notifications for when an SAA is added to or updated in the Static Repository.

The following sections describe the initial version of SAA SR Service, in terms of its service profile, consumer, provider, overall usage, security and quality of service attributes.

## Service Profile

The SAA SR Put Service provides a service interface for the SAA Project Repository to submit new and modified SAA static definitions.  The SAA SR Notification Service then notifies its subscribers via JMS pub/sub topics that new or modified SAAs are present in the SR.  The users of the SAA SR Get Service can then request the static definitions of these specific SAAs.

The service namespaces are:

urn:us:gov:dot:faa:aim:saa:sr:wsdl:SaaGetService

urn:us:gov:dot:faa:aim:saa:sr:wsdl:SaaPutService

The service version is version 1, and the service category according to FAA-STD-066 is Air Transportation Airspace Information Service, ID 1.4.1.  The SAA SR Service is in the development stage currently and will be in the operational stage upon deployment.  The SAA SR Service provides a routine service, as characterized in the NAS-SR-1000.

### Service Provider

The SAA SR Service is provided by Aeronautical Information Management (AIM).  The AIM group is the authoritative government source for collecting, validating, storing, maintaining, and disseminating aeronautical data concerning the United States and its territories to support real-time aviation activities.

#### Point of Contact

Douglas Sage

Automation Specialist, Aeronautical Information Services (AIS) Automation, AJR-32

Doug.Sage@faa.gov

### Service Consumers

Special Activity Airspace Project Repository, AIM.

Special Activity Airspace Operational Repository Service, AIM.

En Route Automation Modernization (ERAM).

### Service Functionality

The SAA SR Service provides the ability to insert new and update existing static definitions of SAAs as well as provide the ability to retrieve these static definitions on request.  The SAA SR Service also provides a pub/sub topic that notifies subscribers when an SAA static definition has been added or changed.

The existing management of SUA definitions exchanges the definitions using different data formats, and at times using manual methods (sending a CD through the mail). The SAA SR Service will enforce a consistent, human readable data exchange format, and an entirely electronic means of transmitting SAA definition information.

### Security

Section redacted.

#### Roles

The first version of the SAA SR Service has two roles:

SAA Approver – Users who can update or submit a new SAA to the SAA SR Service.

SAA Static Data Reader – Users who can request SAA definitions from the SAA SR Service.

#### Access Control Mechanisms

The SAA SR Service will restrict access to its web services through user authentication on each service call.  A username/password combination will be contained in the SOAP header in each request to the service.

Access control to the SR Notification Service requires the JMS client to provide username/password.

#### Security Policies

The SAA SR Service is in compliance to the SWIM WS-I Basic Security Profile 1.1.

### Quality of Service

The SAA SR Service meets the following quality of service parameters:

TBL 4-1
SAA SR Service Quality of Service Parameters

| QoS Parameter | Definition | Value |
| --- | --- | --- |
| Availability | A measure of the lowest probability that a system or constituent piece will be operational during any randomly selected period of time, or, alternatively, the fraction of the total available operating time that the system or constituent piece is operational. | .9975 |

### WSDL Documents

There are two WSDL documents, one for the SaaStaticRepositoryPutService and one for the SaaStaticRepositoryGetService.  The WSDL documents are provided through the namespace listed in section 4.1.

They are also available through the following links:

SAA SR Put Service:

https://swimwiki.tc.faa.gov/download/attachments/6881321/SAAStatic-PutService.wsdl

SAA SR Get Service:

https://swimwiki.tc.faa.gov/download/attachments/6881321/SAAStatic-GetService.wsdl

## Service Interfaces

The service interfaces section defines the data element types, messages exchanged, operations available, and interface provided in this version of the SAA SR Service.

### Types

TBL 4-2 defines the data elements (types) used in the requests to and responses from the SAA SR Service for submissions.  Each data element of a complex type, then lists out the sub data elements that it is composed of.

TBL 4-2
SAA SR Put Service Data Elements

| Data Element | Sub Data Element | Element Definition | Occurrence | Obligation | Description |
| --- | --- | --- | --- | --- | --- |
| Fault |  | A Fault containing the reason why a service call is not successful. |
|  | Body | String | 1 | Required | A description of the fault. |
| InsertSaa Request |  | Used to submit an SAA for insert into the SAA SR. |
|  | SaaMessage | AIXM SaaMessage Object | 1 | Required | An AIXM object that contains the definition of the SAA. Detailed in Appendix A. |
| InsertSaa Response |  | Used confirm if an SAA insert was successful. |
|  | Success | boolean | 1 | Required | Indicates success. |
|  | Uuid | String | 1 | Required | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | Codespace | String | 1 | Required | A URN used to resolve the UUID. |
|  | Type | String Possible Values: SUA ATCAA SAA_COMPONENT | 1 | Required | The type of SAA submitted. |
|  | Designator | String | 1 | Required | The designator of the SAA that was submitted to the service for insertion. |
| UpdateSaaRequest |  | Used to submit an SAA update to the SAA SR. |
|  | SaaMessage | AIXM SaaMessage Object | 1 | Required | An AIXM object that contains the definition of the SAA. Detailed in Appendix A. |
| UpdateSaaResponse |  | Used to confirm if an SAA update was successful. |
|  | success | boolean | 1 | Required | Indicates success. |
|  | uuid | String | 1 | Required | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Required | A URN used to resolve the UUID. |
|  | type | Possible String values: SUA ATCAA SAA_COMPONENT | 1 | Required | The type of SAA submitted. |
|  | designator | String | 1 | Required | The designator of the SAA that was submitted to the service for update. |
| InsertUnitRequest |  | Used to submit a Unit for insert into the SAA SR. |
|  | SaaMessage | AIXM SaaMessage Object | 1 | Required | An AIXM object that contains the definition of the Unit. Detailed in Appendix A. |
| InsertUnitResponse |  | Used confirm if a Unit insert was successful. |
|  | success | boolean | 1 | Required | Indicates success. |
|  | uuid | String | 1 | Required | The Universally Unique Identifier of the Unit. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Required | A URN used to resolve the UUID. |
|  | name | String | 1 | Required | The name of the Unit submitted. |
|  | type | Possible String values: MIL MILOPS OTHER | 1 | Required | The type of Unit submitted. |

TBL 4-3
SAA SR Get Service Data Elements

| Data Element | Sub Data Element | Element Definition | Occurrence | Obligation | Description |
| --- | --- | --- | --- | --- | --- |
| Fault |  | A Fault containing the reason why a service call is not successful. |
|  | body | String | 1 | Required | A description of the fault. |
| UuidKeyType |  | The unique key for a UUID. A string that is unique within the paired codespace that uniquely identifies a specific entity (i.e., SAA, Unit). |
|  | uuid | String | 1 | Required | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Optional | A URN used to resolve the UUID. |
| SaaKeyType |  | The key for an SAA. |
|  | name | String | 1 | Optional | The name of the SAA. |
|  | uuid | String | 1 | Optional | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Optional | A URN used to resolve the UUID. |
| SaaUuidType |  | A combination of the SAA name and type. |
|  | name | String | 1 | Required | The name of the SAA. |
|  | type | saaType Possible values: SUA ATCAA SAA_COMPONENT | 1 | Required | The type of SAA. |
| UnitKeyType |  | The key data for a Unit. |
|  | uuid | String | 1 | Optional | The Universally Unique Identifier of a Unit. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Optional | A URN used to resolve the UUID. |
|  | name | String | 1 | Optional | The name of the Unit. |
|  | designator | String | 1 | Optional | The designator for the Unit. |
| SaaUuid Element |  | Used in the retrieval of the UUID of an SAA. |
|  | name | String | 1 | Optional | The name of the SAA. |
|  | type | String | 1 | Optional | The type of the SAA. |
| GetUuid Request |  |  |  |  | Used to retrieve a requested number of new UUIDs. |
|  | count | int | 1 | Required | The number of UUIDs requested. |
| GetUuid Response |  | Used to return a set of new UUIDs to the service consumer. |
|  | UuidKey | UuidKeyType | Maximum of 100 | Required | The Universally Unique Identifier. A 32 character string that is used to uniquely identify an AIXM feature within a codespace. |
| GetSaaByUuidRequest |  | Used to request an SAA with a specific UUID. |
|  | uuid | string | 1 | Required | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | string | 1 | Required | A URN used to resolve the UUID. |
|  | startTime | dateTime | 1 | Optional | The start time of the interval that the SAA request is for. |
|  | endTime | dateTime | 1 | Optional | The end time of the interval that the SAA request is for. |
| GetSaaByUuidResponse |  | Used to return a requested SAA to the service consumer. |
|  | SaaMessage | AIXM SaaMessage Object | 1 | Required | An AIXM object that contains the definition of the SAA. Detailed in Appendix A. |
| GetSaaNamesRequest |  | A request to get a list of all active and pending SAA names. There are no sub data elements. |
| GetSaaNamesResponse |  | A response containing the keys for all active and pending SAAs. |
|  | SaaKey | SaaKeyType | Unbounded | Optional | The key for an SAA. |
| GetSaaUuid Request |  | The given SAA name and type used to get the UUID |
|  | SaaUuidElement | SaaUuidElement | 1 | Required | The SAA name and type |
| GetSaaUuid Response |  | The response containing the UUID for the given SAA. |
|  | uuid | String | 1 | Required | The Universally Unique Identifier of the SAA. A 32 character string that uniquely identifies an AIXM feature within a codespace. |
|  | codespace | String | 1 | Required | A URN used to resolve the UUID. |
| GetUnits Request |  | A request to get a list of all Units. There are no sub data elements. |
| GetUnits Response |  | A list of Unit data. |
|  | UnitKey | UnitKeyType | Unbounded | Optional | The key information for a Unit. |
| ValidateSaa Request |  | An SAA definition sent in to be validated. |
|  | SaaMessage | AIXM SaaMessage Object | 1 | Required | An AIXM object that contains the definition of the SAA. Detailed in Appendix A. |
| ValidateSaa Response |  | Whether a submitted SAA is valid or not and why. |
|  | success | Boolean | 1 | Required | Indicates success. |
|  | message | String | 1 | Optional | The reason why an SAA is invalid. |

### Messages

TBL 4-4 defines the messages sent between the SAA SR Put Service and its users.

TBL 4-4
SAA SR Put Service Message Descriptions

| Name | Definition | Data Elements (Parts) | Direction |
| --- | --- | --- | --- |
| UpdateSaaRequest | Used by the SAA Project Repository to submit an SAA update. | UpdateSaaRequest | SAA Project Repository -> SAA SR |
| UpdateSaaResponse | Used by the SAA SR Service to respond with if an SAA update is successful or not. | UpdateSaaResponse | SAA SR -> SAA Project Repository |
| InsertSaaRequest | Used by the SAA Project Repository to submit an SAA insert. | InsertSaaRequest | SAA Project Repository -> SAA SR |
| InsertSaaResponse | Used by the SAA SR Service to respond with if an SAA insert is successful or not. | InserSaaResponse | SAA SR -> SAA Project Repository |
| InsertUnitRequest | Used by the SAA Project Repository to submit a Unit insert. | InsertUnitRequest | SAA Project Repository -> SAA SR |
| InsertUnitResponse | Used by the SAA SR Service to respond with if a Unit insert is successful or not. | InsertUnitResponse | SAA SR -> SAA Project Repository |
| Fault | Used by the SAA SR Service when a call is invalid or an error occurs. | Fault | SAA SR -> Service User |

Table 4-5 defines the messages sent between the SAA SR Get Service and its users.

TBL 4-5
SAA SR Get Service Message Descriptions

| Name | Definition | Data Elements (Parts) | Direction |
| --- | --- | --- | --- |
| GetSaaNamesRequest | Used by a user to request a list of SAA names. | GetSaaNamesRequest | Service User -> SAA SR |
| GetSaaNamesResponse | Used by the SAA SR Service to return a list of SAA names. | GetSaaNamesResponse | SAA SR -> Service User |
| GetUnitsRequest | Used by a user to request a list of Units. | GetUnitsRequest | Service User -> SAA SR |
| GetUnitsResponse | Used by the SAA SR Service to return a list of Units. | GetUnitsResponse | SAA SR -> Service User |
| GetSaaByUuidRequest | Used by a user to request an SAA with a given UUID. | GetSaaByUuidRequest | Service User -> SAA SR |
| GetSaaByUuidResponse | Used by the SAA SR Service to return an SAA with a given UUID. | GetSaaByUuidResponse | SAA SR -> Service User |
| GetSaaUuidRequest | Used by a user to request the UUID of an SAA with the given name and type. | GetSaaUuidRequest | Service User -> SAA SR |
| GetSaaUuidResponse | Used by the SAA SR Service to return the UUID of an SAA. | GetSaaUuidResponse | SAA SR -> Service User |
| GetUuidRequest | Used by a user to request a set of unused UUIDs. | GetUuidRequest | Service User -> SAA SR |
| GetUuidResponse | Used by the SAA SR Service to return a set of unused UUIDs. | GetUuidResponse | SAA SR -> Service User |
| ValidateSaaRequest | Used by a user to validate a submitted SAA definition. | ValidateSaaRequest | Service User -> SAA SR |
| ValidateSaaResponse | Used by the SAA SR Service to return whether or not a submitted SAA definition is valid. | ValidateSaaResponse | SAA SR -> Service User |
| Fault | Used by the SAA SR Service when a call is invalid or an error occurs. | Fault | SAA SR -> Service User |

#### Error Codes

The error codes used in response messages from the service are To Be Determined (TBD), but will be listed in TBL 4-6.

TBL 4-6
SAA SR Get Service Message Descriptions

| Error Code | Description |
| --- | --- |

### Operations

#### SAA SR Put Service Operations

The following tables describe the operations provided by the SAA SR Put Service.

TBL 4-7
insertSaa Operation Description

| Operation Name | insertSaa |
| --- | --- |
| Description | Allows the user to submit a static definition for a new SAA to the SAA Static Repository. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service consumer, the SAA Project Repository, has a correctly implemented application for creating the SAA insert request. Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message InsertSaaRequest. |
| Output | Message InsertSaaResponse, or SOAP Fault Message. |
| Effect | The submitted SAA static definition is inserted into the SAA Static Repository. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-8
updateSaa Operation Description

| Operation Name | updateSaa |
| --- | --- |
| Description | Allows the user to submit a static definition for an existing SAA to the SAA Static Repository. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service consumer, the SAA Project Repository, has a correctly implemented application for creating the SAA update request. Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message UpdateSaaRequest. |
| Output | Message UpdateSaaResponse, or SOAP Fault Message. |
| Effect | The submitted SAA static definition is updated into the SAA Static Repository. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-9
insertUnit Operation Description

| Operation Name | insertUnit |
| --- | --- |
| Description | Allows the user to submit a definition for a new Unit to the SAA Static Repository. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service consumer, the SAA Project Repository, has a correctly implemented application for creating the Unit insert request. Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message InsertUnitRequest. |
| Output | Message InsertUnitResponse, or SOAP Fault Message. |
| Effect | The submitted Unit definition is inserted into the SAA Static Repository. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

#### SAA SR Get Service Operations

The following tables describe the operations provided by the SAA SR Get Service.

TBL 4-10
getNewUuid Operation Description

| Operation Name | getNewUuid |
| --- | --- |
| Description | Allows the user to request a given number of unused UUIDs. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message GetUuidRequest. |
| Output | Message GetUuidResponse, or SOAP Fault Message. |
| Effect | A set of unused UUIDs are sent to the service consumer for their use. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-11
getSaaByUuid Operation Description

| Operation Name | getSaaByUuid |
| --- | --- |
| Description | Allows the service consumer to get the static definition of the SAA with a given UUID for a given time period. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message GetSaaByUuidRequest. |
| Output | Message GetSaaByUuidResponse, or SOAP Fault Message. |
| Effect | The static definition of the requested SAA for the requested time period is returned to the service consumer. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-12
getSaaNames Operation Description

| Operation Name | getSaaNames |
| --- | --- |
| Description | Allows the service consumer to get a collection of names for all active and pending SAAs in the Static Repository. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message GetSaaNamesRequest. |
| Output | Message GetSaaNamesResponse, or SOAP Fault Message. |
| Effect | A collection of all SAA names in the SAA Static Repository is returned to the service consumer. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-13
getSaaUUID Operation Description

| Operation Name | getSaaUuid |
| --- | --- |
| Description | Allows the service consumer to submit key information of an SAA (name and type) to retrieve the SAA’s UUID. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message GetSaaUuidRequest. |
| Output | Message GetSaaUuidResponse, or SOAP Fault Message. |
| Effect | The UUID of the SAA with the matching key information is returned to the service consumer. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1 |

TBL 4-14
getUnits Operation Description

| Operation Name | getUnits |
| --- | --- |
| Description | Allows the service consumer to get a collection of all active and pending Unit objects in the SAA Static Repository. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message GetUnitsRequest. |
| Output | Message GetUnitsResponse, or SOAP Fault Message. |
| Effect | A collection of all the Unit objects in the SAA Static Repository is returned to the service consumer. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

TBL 4-15
validateSaa Operation Description

| Operation Name | validateSaa |
| --- | --- |
| Description | Allows the user to submit a static definition of an SAA and have the SAA SR Service validate it. |
| MEP | In-Out (FAA-STD-066 Message Exchange Pattern Taxonomy) |
| Precondition | Service provider SAA SR Service has the service consumer identified as an authorized service consumer. |
| Input | Message ValidateSaaRequest. |
| Output | Message ValidateSaaResponse, or SOAP Fault Message. |
| Effect | The service consumer receives a response saying whether or not the submitted SAA is valid, and if it’s not, a reason why it is not valid. |
| Faults | TBD, but will be identified from the pre-defined error messages in section 4.2.2.1. |

### Lists of Interfaces

The SAA Project Repository submits static definitions of SAAs to the SAA Static Repository via web service-based message transfer.

Other service consumers submit requests for information related to SAAs to the SAA SR Service via web service-based message transfer.

The SAA SR Notification Service publishes notifications of SAA updates to a JMS topic. Users that subscribe to that JMS topic then receive these notifications. Note: The interface description for the JMS topic is not written, but will be referenced here when it is.

TBL 4-16 below lists the two interfaces being implemented in the SAA SR Service.

TBL 4-16
List of Interfaces

| Name | Description | Operations |
| --- | --- | --- |
| SaaStaticRepositoryPutPort | Allows the SAA Project Repository to submit SAAs and Units to the SAA SR Service to store in the Static Repository. | insertSaa updateSaa insertUnit |
| SaaStaticRepositoryGetPort | Allows service consumers to retrieve information on SAAs as well as have the service evaluate a SAA definition they submit to see if it is a valid definition. | getNewUuid getSaaByUuid getSaaNames getSaaUuid getUnits validateSaa |
| SaaStaticRepositoryNotificationPort | Allows users to subscribe to JMS topics in order to receive notifications that new or modified SAAs are available through the SAA SR Get Service. |  |

## Service Implementation

The SAA SR Service complies with cited SWIM Segment 1 Compliance standards for web service protocols listed in Section 2.1, Standards for FAA SWIM Program Compliance.

The SAA SR Service will be hosted at the Mike Monroney Aeronautical Center in Oklahoma City.  The backup of the system will be hosted at the William J. Hughes Technical Center in Atlantic City.  The hardware and its configuration is currently TBD, so the specific end point addresses are also TBD.

The SAA SR Service interface complies with web services interface standards Web Service Definition Language (WSDL), and SOAP.  The SAA SR Service transports messages over a HyperText Transfer Protocol with SSL (HTTPS) session.

### End Points

The following sections describe the associated interface, communication protocol, messaging protocol, and network address.

#### SAA SR Put Service End Points

##### Associated Interface

For all SAA SR Put Service end points, the interface name is SaaStaticRepositoryPutPort.

##### Communication Protocol

For all SAA SR Put Service end points, the communications protocol is HTTPS.

##### Messaging Protocol

For all SAA SR Put Service end points, the messaging protocol is SOAP.

##### Network Address

The network address for the SAA SR Put Service interface is currently TBD.

##### End Point-Specific Qualities of Service

TBL 4-17
SAA SR Put Service Quality of Service Parameters

| QoS Parameter | Definition | Value |
| --- | --- | --- |
| Response Time for insertSaa and updateSaa operations. | A measure of the longest average time period required to complete a service request, from the time the requester invokes the service to the time the requester receives the last byte of the response. | A 95th percentile response time of 10 seconds per airspace volume per timeslice. |
| Response Time for insertUnit operation. | A measure of the longest average time period required to complete a service request, from the time the requester invokes the service to the time the requester receives the last byte of the response. | A 95th percentile response time of 10 seconds. |

#### SAA SR Get Service End Points

##### Associated Interface

For all SAA SR Get Service end points, the interface name is SaaStaticRepositoryGetPort.

##### Communication Protocol

For all SAA SR Get Service end points, the communications protocol is HTTPS.

##### Messaging Protocol

For all SAA SR Get Service end points, the messaging protocol is SOAP.

##### Network Address

The network address for the SAA SR Get Service interface is currently TBD.

##### End Point-Specific Qualities of Service

TBL 4-18
SAA SR Service Quality of Service Parameters

| QoS Parameter | Definition | Value |
| --- | --- | --- |
| Response Time for get services | A measure of the longest average time period required to complete a service request, from the time the requester invokes the service to the time the requester receives the last byte of the response. | A 95th percentile response time of 5 seconds. |
| Response Time for the validateSaa operation | A measure of the longest average time period required to complete a service request, from the time the requester invokes the service to the time the requester receives the last byte of the response. | A 95th percentile response time of 10 seconds per airspace volume per timeslice. |

#### SAA SR Notification Service End Points

##### Associated Interface

For all SAA SR Notification Service end points, the interface name is SaaStaticRepositoryNotificationPort.

##### Communication Protocol

For all SAA SR Notification Service end points, the communications protocol is TCP/IP (with SSL/TLS).

##### Messaging Protocol

For all SAA SR Notification Service end points, the messaging protocol is SOAP.

The JMS client must be a FUSE message broker in order to receive updates from the service.

##### Network Address

The network address for the SAA SR Notification Service interface is currently TBD.

##### End Point-Specific Qualities of Service

TBL 4-19
SAA SR Notification Service Quality of Service Parameters

| QoS Parameter | Definition | Value |
| --- | --- | --- |
| Response Time | A measure of the longest average time period required to complete a service request, from the time the requester invokes the service to the time the requester receives the last byte of the response. | Responds within 5 seconds or less of an update, insert, or invalidation of an SAA. |

Accepted Data Elements

The accepted AIXM elements for the SAA SR Service are defined in Appendix C of the AIM SAA Management Web Services IRD.

The accepted ways to define geometries for SAAs in GML are defined in Appendix D of the AIM SAA Management Web Services IRD.