## Slide 1: Improving Access to Point Cloud Data
98th OGC Technical Committee
Washington DC, USA
8 March 2016
Keith Ryden
Esri Software Development
kryden@esri.com

## Slide 2: Topics
Point Cloud Data
Access through Services
LAS data
  Optimization without changing the LAS file
  Redefining LAS data storage
Summary

## Slide 3: Point Cloud Data
Multi-dimensional Scientific data
LiDAR Data
Elevation Data
Seismic Data
Bathymetric Data
Meteorological Data
Fixed/Mobile consumer sensors (IoT)
It’s not just LiDAR
Notes: <number>

## Slide 4: There’s Lots of it…
Point Cloud data is typically Big Data
  LiDAR data in a collection of LAS datasets are one example
  It’s big if you don’t want to move it….
  Bring the processing to the data….
The amount of data is so large that repeated conversion, import, transport, etc., can be painful

## Slide 5
Enterprise Imagery and Point Cloud Management – Access through Services
MSI/HSl
LIDAR
EO
CIR
FMV
Multiple Sensors & Formats
OGC Services WCS, WMS, WPS, WCPS, etc
Data Formats KML, LAS, GML
Store it Once, Use it Many Times
Notes: <number>

## Slide 6: Point Cloud Services
Enterprise Point Cloud data services need to support:
  Standardized Service Interfaces
  Overlapping collections
  Collections over time
  Arbitrary query areas
  High performance access
  Efficient transfer format/schema
  Efficient storage, backup, recovery
  Elastic deployment

## Slide 7: LAS Data
The LAS format is a data transfer/exchange format
  Well understood, and widely supported
  Not originally designed for direct use/exploitation
Issues when accessed directly include
  Simple format (a plus) but becomes an I/O bottleneck
  Lack of spatial index
  Lack of dataset statistics
  Uncompressed
  Huge files – even when compressed

## Slide 8: Improving Access To LAS
Start simple –
  No changes to the LAS file
  Add a “sidecar” file that has all the optimization information in it
    Metadata
    Classification
    Statistics
    Spatial Indexing
    Reorganize records
Get more complicated later –
  Redefine the LAS file storage
    SQL is your friend – RDBMS and SQLite
    Make it continuous and scalable
    Compression
Copyright © 2016 Open Geospatial Consortium

## Slide 9: Sidecar File
Copyright © 2016 Open Geospatial Consortium
Existing LAS Data file
MyLidarData.las
Metadata Classification Statistics Spatial Index
MyLidarData.lasX
LAS Data File is not modified – allows us to support all existing LAS revisions without compatibility problems
Additional information is stored in the sidecar file, and used by the application to configure the user interface and optimize data access Could be XML, CSV, Binary, or a well defined mix for efficiency

## Slide 10: Point Classification
Copyright © 2016 Open Geospatial Consortium
From ASPRS LAS Specification Version 1.4-R13
LAS defines a set of Classification values
Older format values are a subset of newer values
When reserved or user definable values are used, where are they defined?

## Slide 11: Point Classification
Copyright © 2016 Open Geospatial Consortium
User defined classification values probably end up being recorded in spreadsheets….

## Slide 12: Point Classification
Data Point Classification is easily defined in a portable format – possible info might include:
  Classification Value (integer)
  Classification Name (short string)
  Classification Description (optional, longer description)
  Classification URL (optional, URL to external descriptive resource)
  Point Count (integer)
Well suited for either XML or CSV format
Copyright © 2016 Open Geospatial Consortium

## Slide 13: Fast Spatial Access to Point Records
LAS files consist of variable length records full of individual fixed format point records.
Each record has it’s length and ID encoded in its’ header.
End up scanning the file to find stuff…
We can optimize access to LAS data by spatially indexing the variable length point records based on the extent of the points, using the point record ID as the key.
  Now you know which variable length point records are of interest…
  Read only those, and scan the internal points.
Copyright © 2016 Open Geospatial Consortium

## Slide 14: Spatial Index
Spatial indexing for fast access to data by extent/location. There are
Several indexing possibilities
Grids
Quad Trees
RTrees

## Slide 15: Metadata
Normalize the Metadata so we can use any LAS version
  Lots of Metadata standards
  Generally XML encoded
  Pick one, or allow any well defined community metadata schema
Include the Coordinate Reference Information
  Not consistent across LAS versions
Hash or checksum on the LAS data file?
  Might be a good idea – let’s you know if the file has been changed
Copyright © 2016 Open Geospatial Consortium

## Slide 16: Rearrange Point Records
If individual points are scattered through the LAS file, you can optimize access by rearranging the points
  Cluster points spatially related together
  Reorganize points based on application requirements
  Moves points into different records, but doesn’t change the LAS format…
Copyright © 2016 Open Geospatial Consortium

## Slide 17: Redefining LAS Storage
Define a schema for storing LAS header and point record data that can be supported in most modern commercial and open source RDBMS systems
Using the existing Simple Features SQL spec, we can encode and spatially search Variable Length LAS Point records.
  INTEGER - Record ID value
  GEOMETRY - Polygon or Envelope defining the shape of the Point Record, spatially indexed for fast search ad retrieval
  BLOB - Unmodified Variable Length Point Record
Utilize existing RDBMS capabilities to:
  Manage and partition massive record sets
  Provide multi-user access
  Maintain referential integrity
  Ensure high availability
Use SQLite for a “Personal” or single file LAS data container
Copyright © 2016 Open Geospatial Consortium

## Slide 18: Compress Records of LAS Points
LAS Point Records can be effectively compressed
  Retain LAS Variable Length Record format for uncompressed representation – eliminates lots of application change
  Hide compression behind the GET/SET function in the client library
  Leave the data value compressed during transmission
Copyright © 2016 Open Geospatial Consortium

## Slide 19: Summary
Point Cloud data is Big Data…
  Access via well defined web services
  OGC is well positioned to influence these service specifications
The LAS data format is part of the picture
  An exchange format for LiDAR and similar data
  Access and application interoperability can be improved by introducing a “sidecar” file with metadata, classification, statistics, and spatial index information
  Existing LAS record formats can be retained while taking advantage of RDBMS products for storage, scalability, and multi-user access.

## Slide 20: End
Copyright © 2016 Open Geospatial Consortium